SPARKER DCCDIP2 - mounting instructions for Honda CB400A

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see table). Counterpart connectors are included.

| wire color DCCDIP2 | pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | yellow | IC 1 | inductive coil 1 |
| blue | 2 | green | SENSE GND | ground for sensors |
| violet | 3 |  | FUEL PUMPE RELAY | output for fuel pump relay |
| green | 4 |  | M | output for servomotor |
| green | 5 |  | M | output for servomotor |
| grey | 6 |  | TPS | throttle position sensor |
|  | 7 |  |  |  |
| black | 8 | light blue | INPUT 1 | multifunctional input 1 |
| yellow | 9 | brown | CKPS (1) | input for pick-up (1) |
| white | 10 |  | IC 2 | inductive coil 2 |
| blue | 11 | green | GND | ground |
| violet | 12 |  | GEAR SHIFT LIGHT | output for gear shift light |
| red | 13 |  | + 12 V | supply 12 V |
| pink | 14 |  | POWER JET | Power jet output |
| green/yellow | 15 |  | TACHO | output for tachometer |
| blue | 16 | orange | GND | ground |
| white/red | 17 |  | + 5 V | supply for sensors |
| white/blue | 18 |  | STPS | servo position sensor |
| grey/red | 19 | black/white | INPUT 2 | multifunctional input 1 (used as KILL switch) |
| brown | 20 | pink | CKPS (2) | input for pick-up (2) |

Also is need connect 2x green/black wires from bike to 2x green/black wires on connector adapter.

Also is need connect green/white wire from bike to green/orange wire on connector adapter.

Also is need connect +12V from ignition key switch to red wire on connector adapter.

Residual wires (white and blue from stator) connect so that white connect to ground and blue do not connect.

Producer address: 	IgniTech

Chrudimská 1739

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz