SPARKER DCCDIP2 - mounting instructions for Honda NSR125

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see tables). Counterpart connectors are included.

| wire color DCCDIP2 | pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | yellow/black | IC 1 | inductive coil 1 |
| blue | 2 | green (note 1) | GND | ground, ground for sensors |
|  | 3 |  | POWEROUT 1 | power output 1 |
| green | 4 | white (note 1) | M | output for servomotor |
| green | 5 | white/black (note 1) | M | output for servomotor |
|  | 6 |  | TPS | throttle position sensor |
|  | 7 |  |  |  |
| black | 8 | green/white | INPUT 2 | multifunctional input 2 (use as blocking) |
| yellow | 9 | blue | CKPS (1) | input for pick-up (1) |
|  | 10 |  | IC 2 | inductive coil 2 |
| blue | 11 | green | GND | ground, ground for sensors |
|  | 12 |  | POWEROUT 2 | power output 2 |
| red | 13 | black (note 1) | + 12 V | supply 12 V |
|  | 14 |  | POWEROUT 3 | power output 3 |
| green/yellow | 15 | yellow/black | TACHO | output for tachometer |
| blue | 16 | green/blue (note 1) | SENSE GND |  |
| white/red | 17 | red/white (note 1) | + 5 V | supply for sensors |
| white/blue | 18 | light green (note 1) | STPS | servo position sensor |
| green | 19 | black/white | INPUT 1 | multifunctional input 1 (use as KILL SW.) |
|  | 20 |  | CKPS (2) | input for pick-up (2) |

Note 1:

Outputs for servo you must connect instead original servo controller.