SPARKER DCCDIP2 - mounting instructions for Honda NSR250 MC16

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see table). Counterpart connectors are included.

| pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- |
| 1 | black/yellow | IC 1 | inductive coil 1 |
| 2 | green | GND | ground for sensors |
| 3 | pink (directly on oil pump solenoid) | FUEL PUMPE RELAY | output for fuel pump relay |
| 4 | white/black (directly on servomotor) | M | output for servomotor |
| 5 | white/red (directly on servomotor) | M | output for servomotor |
| 6 |  | TPS | throttle position sensor |
| 7 |  | BLOCK_A | blocking input (neutral sw.) |
| 8 |  | BLOCK | blocking input (sidetand sw.) |
| 9 | yellow | CKPS (1) | input for pick-up (1) |
| 10 | black/blue | IC 2 | inductive coil 2 |
| 11 | green | GND | ground |
| 12 |  | GEAR SHIFT LIGHT | output for gear shift light |
| 13 | black/white | + 12 V | supply 12 V |
| 14 |  | POWER JET | Power jet output |
| 15 |  | TACHO | output for tachometer |
| 16 | white/blue, white/yellow | SENSE GND | sensor ground |
| 17 | white (directly on servomotor) | + 5 V | supply for sensors |
| 18 | light green (directly on servomotor) | STPS | servo position sensor |
| 19 |  | KILL SWITCH | input for kill switch |
| 20 | blue | CKPS (2) | input for pick-up (2) |

1) We don´t know function of oil pump solenoid - must be ON during engine run i think. If yes, connect this to pin 3 please.

2) We don´t know data for exhaust valve.

3) Will be not function tachometer maybe (DCCDIP2 have different signal to inductive coil). If don´t function - you must connect TACHO output (pin 15) and tachometer directly (instead of black/yellow from inductive coil).

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz