SPARKER DCCDIP2 - mounting instructions for Honda XRV750

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see tables). Counterpart connectors are included.

| wire color DCCDIP2 | pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | 2x black/blue (shorter harness on bike) | IC 1 | ignition coil 1 |
| blue | 2 | green/white (longer harness on bike) | GND | ground |
| violet | 3 |  | POWER OUT 1 | multifunctional output 1 |
| green | 4 |  | M | output for servomotor |
| green | 5 |  | M | output for servomotor |
| grey | 6 |  | TPS | throttle position sensor |
|  | 7 |  |  | not used |
| black | 8 | light green/yellow (shorter harness on bike) | INPUT 2 | multifunctional input 2 |
| yellow | 9 | blue/yellow (shorter harness on bike) | CKPS (1) | input for pick-up (1) |
| white | 10 | 2x black/yellow (longer harness on bike) | IC 2 | ignition coil 2 |
| blue | 11 | green (shorter harness on bike) | GND | ground |
| blue/white | 12 |  | POWER OUT 2 | multifunctional output 2 |
| red | 13 | black/white (shorter harness on bike) | + 12 V | supply 12 V |
| pink | 14 |  | POWER OUT 3 | multifunctional output 1 |
| green/yellow | 15 |  | TACHO | output for tachometer |
| blue | 16 |  | SENSE GND | ground for sensors |
| white/red | 17 |  | + 5 V | supply for sensors |
| white/blue | 18 |  | STPS | servo position sensor |
| grey/red | 19 |  | INPUT | multifunctional input 1 |
| brown | 20 | white/yellow (longer harness on bike) | CKPS (2) | input for pick-up (2) |