SPARKER DCCDIP2 - mounting instructions for Suzuki DR600

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see tables). Counterpart connectors are included.

| wire color DCCDIP2 | pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | black | IC 1 | inductive coil 1 |
| blue | 2 | green | GND | ground or ground for sensors |
| violet | 3 |  | POWEROUT 1 | multifunctional output 1 |
| green | 4 |  | M | output for servomotor |
| green | 5 |  | M | output for servomotor |
| grey | 6 |  | TPS | throttle position sensor |
|  | 7 |  |  |  |
| black | 8 |  | INPUT 2 | multifunctional input 2 |
| yellow | 9 | orange | PICK-UP 1 | input for pick-up (1) |
| white | 10 |  | IC 2 | inductive coil 2 |
| blue | 11 | black/white | GND | ground |
| blue/white | 12 |  | POWEROUT 2 | multifunctional output 2 |
| red | 13 | orange from ignition key | + 12 V | supply 12 V |
| pink | 14 |  | POWEROUT 3 | multifunctional output 3 |
| green/yellow | 15 |  | TACHO | output for tachometer |
| blue | 16 |  | SENSE GND | ground for sensors |
| white/red | 17 |  | + 5 V | supply for sensors |
| white/blue | 18 |  | STPS | servo position sensor |
| grey/red | 19 | black/yellow | INPUT 1 | multifunctional input 1 |
| brown | 20 |  | PICK-UP 2 | input for pick-up (2) |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz