SPARKER DCCDIP2 - mounting instructions for Suzuki GSXR750 1998 (inj. to carb.)

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see tables). Counterpart connectors are included.

| pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- |
| 1 | yellow (18pin connector) | IC | inductive coil 1 |
| 2 | grey (18pin connector) | GND | ground (for IG) |
| 3 | yellow/black (18pin connector) | FUEL PUMPE RELAY | output for fuel pump relay |
| 4 |  | M | output for servomotor |
| 5 |  | M | output for servomotor |
| 6 | blue (24pin connector) | TPS | throttle position sensor |
| 7 |  | INPUT 2A | input 2 (through diode) |
| 8 |  | INPUT 2 | input 2 |
| 9 | black (24pin connector) | CKPS (1) | input for pick-up (1) |
| 10 | green (18pin connector) | IC 2 | inductive coil 2 |
| 11 | black/white (18pin connector) | GND | ground |
| 12 |  | GEAR SHIFT LIGHT | output for gear shift light |
| 13 | orange/white (18pin connector) | + 12 V | supply 12 V |
| 14 |  | POWER OUT 3 | Power output 3 |
| 15 | black/red (18pin connector) | TACHO | output for tachometer |
| 16 | green, black/brown (24pin connector) | SENSE GND | ground (for sensors) |
| 17 | red (24pin connector) | + 5 V | supply for sensors |
| 18 |  | STPS | servo position sensor |
| 19 |  | INPUT 1 | input 1 |
| 20 |  | CKPS (2) | input for pick-up (2) |