SPARKER DCCDIP2 - mounting instructions for Suzuki RGV250

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see tables). Counterpart connectors are included.

Our unit have no output for carburator solenoids. If is possible - you can use GEAR SHIFT LIGHT and POWER JET output for control of this solenoids.

You must set working area of TPS (0 and 100 %) and servo of exhaust valve.

K type

| pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- |
| 1 | black/yellow | IC 1 | inductive coil 1 |
| 2 | black (from pickups) | GND | ground (use for pickup gnd) |
| 3 |  | POWEROUT 1 | power output 1 |
| 4 |  | M | output for servomotor |
| 5 |  | M | output for servomotor |
| 6 |  | TPS | throttle position sensor |
| 7 |  |  |  |
| 8 |  | INPUT 2 | multifunctional input 2 |
| 9 | red | PICK-UP 1 | input for pick-up 1 |
| 10 | white/blue | IC 2 | inductive coil 2 |
| 11 | black/white | GND | power ground |
| 12 |  | POWEROUT 2 | power output 2 |
| 13 | orange/black | + 12 V | supply 12 V |
| 14 |  | POWEROUT 3 | power output 3 |
| 15 |  | TACHO | output for tachometer |
| 16 | white (from pickups) | SENSE GND | ground for sensors |
| 17 |  | + 5 V | supply for sensors |
| 18 |  | STPS | servo position sensor |
| 19 |  | INPUT 1 | multifunctional input 1 |
| 20 | brown | PICK-UP 2 | input for pick-up 2 |

you must interconnect blue (NEUTRAL switch) and blue/black (NEUTRAL indicator)

L type (replace both original units - remove original CDI unit is necessary)

| pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- |
| 1 | black/yellow (direct to IC) | IC 1 | inductive coil 1 |
| 2 | white (from pickups) black (from pickups) | GND | ground (use for pickup gnd) |
| 3 |  | POWEROUT 1 | power output 1 |
| 4 | black/red | M | output for servomotor |
| 5 | red/black | M | output for servomotor |
| 6 | blue (from TPS) | TPS | throttle position sensor |
| 7 |  |  |  |
| 8 |  | INPUT 2 | multifunctional input 2 |
| 9 | red | PICK-UP 1 | input for pick-up 1 |
| 10 | white/blue (direct to IC) | IC 2 | inductive coil 2 |
| 11 | black/white | GND | power ground |
| 12 |  | POWEROUT 2 | power output 2 |
| 13 | orange/black | + 12 V | supply 12 V |
| 14 |  | POWEROUT 3 | power output 3 |
| 15 |  | TACHO | output for tachometer |
| 16 | black/white (from TPS) black/white (from STPS) | SENSE GND | ground for sensors |
| 17 | orange (from STPS) orange (from STPS) | + 5 V | supply for sensors |
| 18 | yellow | STPS | servo position sensor |
| 19 |  | INPUT 1 | multifunctional input 1 |
| 20 | brown | PICK-UP 2 | input for pick-up 2 |

you must interconnect blue (NEUTRAL switch) and blue/black (NEUTRAL indicator)

M type (replace both original units - remove original CDI unit is necessary, without solenoids drive)

| pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- |
| 1 | black/yellow (direct to IC) | IC 1 | inductive coil 1 |
| 2 | white (from pickups) | GND | ground (use for pickup gnd) |
| 3 |  | POWEROUT 1 | power output 1 |
| 4 | black/red | M | output for servomotor |
| 5 | red/black | M | output for servomotor |
| 6 | blue (from TPS) | TPS | throttle position sensor |
| 7 |  |  |  |
| 8 |  | INPUT 2 | multifunctional input 2 |
| 9 | red | PICK-UP 1 | input for pick-up 1 |
| 10 | white/blue (direct to IC) | IC 2 | inductive coil 2 |
| 11 | black/white | GND | power ground |
| 12 |  | POWEROUT 2 | power output 2 |
| 13 | orange/black | + 12 V | supply 12 V |
| 14 |  | POWEROUT 3 | power output 3 |
| 15 | white/red | TACHO | output for tachometer |
| 16 | black/green | SENSE GND | ground for sensors |
| 17 | orange/white | + 5 V | supply for sensors |
| 18 | yellow | STPS | servo position sensor |
| 19 |  | INPUT 1 | multifunctional input 1 |
| 20 | brown | PICK-UP 2 | input for pick-up 2 |

you must interconnect blue (NEUTRAL switch) and blue/black (NEUTRAL indicator)

approximately 1996 (replace both original units - remove original CDI unit is necessary, without solenoids drive)

| pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- |
| 1 | black/yellow (direct to IC) | IC 1 | inductive coil 1 |
| 2 | white (from pickups) | GND | ground (use for pickup gnd) |
| 3 |  | POWEROUT 1 | power output 1 |
| 4 | red/grey | M | output for servomotor |
| 5 | red/black | M | output for servomotor |
| 6 | blue (from TPS) | TPS | throttle position sensor |
| 7 |  |  |  |
| 8 |  | INPUT 2 | multifunctional input 2 |
| 9 | red | PICK-UP 1 | input for pick-up 1 |
| 10 | white/blue (direct to IC) | IC 2 | inductive coil 2 |
| 11 | white/black (rather black/white) | GND | power ground |
| 12 |  | POWEROUT 2 | power output 2 |
| 13 | orange/black | + 12 V | supply 12 V |
| 14 |  | POWEROUT 3 | power output 3 |
| 15 |  | TACHO | output for tachometer |
| 16 | black/green | SENSE GND | ground for sensors |
| 17 | orange | + 5 V | supply for sensors |
| 18 | yellow | STPS | servo position sensor |
| 19 |  | INPUT 1 | multifunctional input 1 |
| 20 | brown | PICK-UP 2 | input for pick-up 2 |

you must interconnect blue (NEUTRAL switch) and blue/black (NEUTRAL indicator)

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz