SPARKER DCCDIP2 - mounting instructions for Suzuki RGV250

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see tables). Counterpart connectors are included.

Our unit have no output for carburator solenoids. If is possible - you can use GEAR SHIFT LIGHT and POWER JET output for control of this solenoids.

You must set working area of TPS (0 and 100 %) and servo of exhaust valve.

K type

| wire color DCCDIP2 | pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | black/yellow | IC 1 | inductive coil 1 |
| blue | 2 | white (from pickups) black (from pickups) | SENSE GND | ground for sensors |
| violet | 3 |  | FUEL PUMP RELAY | output for fuel pump relay |
| green | 4 |  | M | output for servomotor |
| green | 5 |  | M | output for servomotor |
| grey | 6 |  | TPS | throttle position sensor |
|  | 7 | black + black/blue | BLOCK_A | blocking input (neutral sw.) |
| black | 8 | green | BLOCK | blocking input (sidetand sw.) |
| yellow | 9 | red | CKPS (1) | input for pick-up (1) |
| white | 10 | white/blue | IC 2 | inductive coil 2 |
| blue | 11 | black/white | GND | ground |
|  | 12 |  | GEAR SHIFT LIGHT | output for gear shift light |
| red | 13 | orange/black | + 12 V | supply 12 V |
|  | 14 |  | POWER JET | Power jet output |
| green/yellow | 15 |  | TACHO | output for tachometer |
|  | 16 |  |  |  |
| white/red | 17 |  | + 5 V | supply for sensors |
| white/blue | 18 |  | STPS | servo position sensor |
|  | 19 |  | KILL SWITCH | input for kill switch |
| brown | 20 | brown | CKPS (2) | input for pick-up (2) |

L type (replace both original units - remove original CDI unit is necessary)

| wire color DCCDIP2 | pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | black/yellow (direct to IC) | IC 1 | inductive coil 1 |
| blue | 2 | white (from pickups) black (from pickups) black/white (from TPS) black/white (from STPS) | SENSE GND | ground for sensors |
| violet | 3 |  | FUEL PUMP RELAY | output for fuel pump relay |
| green | 4 | black/red | M | output for servomotor |
| green | 5 | red/black | M | output for servomotor |
| grey | 6 | blue (from TPS) | TPS | throttle position sensor |
|  | 7 | black (rather blue) black/blue | BLOCK_A | blocking input (neutral sw.) |
| black | 8 | green | BLOCK | blocking input (sidetand sw.) |
| yellow | 9 | red | CKPS (1) | input for pick-up (1) |
| white | 10 | white/blue (direct to IC) | IC 2 | inductive coil 2 |
| blue | 11 | black/white | GND | ground |
|  | 12 |  | GEAR SHIFT LIGHT | output for gear shift light |
| red | 13 | orange/black | + 12 V | supply 12 V |
|  | 14 |  | POWER JET | Power jet output |
| green/yellow | 15 |  | TACHO | output for tachometer |
|  | 16 |  |  |  |
| white/red | 17 | orange (from STPS) orange (from TPS) | + 5 V | supply for sensors |
| white/blue | 18 | yellow | STPS | servo position sensor |
|  | 19 |  | KILL SWITCH | input for kill switch |
| brown | 20 | brown | CKPS (2) | input for pick-up (2) |

M type (replace both original units - remove original CDI unit is necessary, without solenoids drive)

| wire color DCCDIP2 | pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | black/yellow (direct to IC) | IC 1 | inductive coil 1 |
| blue | 2 | white (from pickups) black/green | SENSE GND | ground for sensors |
| violet | 3 |  | FUEL PUMP RELAY | output for fuel pump relay |
| green | 4 | black/red | M | output for servomotor |
| green | 5 | red/black | M | output for servomotor |
| grey | 6 | blue (from TPS) | TPS | throttle position sensor |
|  | 7 | blue + blue/black | BLOCK_A | blocking input (neutral sw.) |
| black | 8 | green | BLOCK | blocking input (sidetand sw.) |
| yellow | 9 | red | CKPS (1) | input for pick-up (1) |
| white | 10 | white/blue (direct to IC) | IC 2 | inductive coil 2 |
| blue | 11 | black/white | GND | ground |
|  | 12 |  | GEAR SHIFT LIGHT | output for gear shift light |
| red | 13 | orange/black | + 12 V | supply 12 V |
|  | 14 |  | POWER JET | Power jet output |
| green/yellow | 15 | white/red | TACHO | output for tachometer |
|  | 16 |  |  |  |
| white/red | 17 | orange/white | + 5 V | supply for sensors |
| white/blue | 18 | yellow | STPS | servo position sensor |
|  | 19 |  | KILL SWITCH | input for kill switch |
| brown | 20 | brown | CKPS (2) | input for pick-up (2) |

approximately 1996 (replace both original units - remove original CDI unit is necessary, without solenoids drive)

| wire color DCCDIP2 | pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | black/yellow (direct to IC) | IC 1 | inductive coil 1 |
| blue | 2 | white (from pickups) green/black (rather black/green) | SENSE GND | ground for sensors |
| violet | 3 |  | FUEL PUMP RELAY | output for fuel pump relay |
| green | 4 | red/grey | M | output for servomotor |
| green | 5 | red/black | M | output for servomotor |
| grey | 6 | blue (from TPS) | TPS | throttle position sensor |
|  | 7 | blue blue/black | BLOCK_A | blocking input (neutral sw.) |
| black | 8 | green/brown | BLOCK | blocking input (sidetand sw.) |
| yellow | 9 | red | CKPS (1) | input for pick-up (1) |
| white | 10 | white/blue (direct to IC) | IC 2 | inductive coil 2 |
| blue | 11 | white/black (rather black/white) | GND | ground |
|  | 12 |  | GEAR SHIFT LIGHT | output for gear shift light |
| red | 13 | orange/black | + 12 V | supply 12 V |
|  | 14 |  | POWER JET | Power jet output |
| green/yellow | 15 |  | TACHO | output for tachometer |
|  | 16 |  |  |  |
| white/red | 17 | orange | + 5 V | supply for sensors |
| white/blue | 18 | yellow | STPS | servo position sensor |
|  | 19 |  | KILL SWITCH | input for kill switch |
| brown | 20 | brown | CKPS (2) | input for pick-up (2) |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz