SPARKER DCCDIP2 - mounting instructions for

Yamaha TZR125 4FL-SF1

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see table).

| wire color DCCDIP2 | pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | orange | IC 1 | inductive coil 1 |
| blue | 2 | white/red | SENSE GND | ground for sensors |
|  | 3 |  | POWEROUT 1 | poweroutput 1 (fuel pump relay) |
| green | 4 |  | M | output for servomotor |
| green | 5 |  | M | output for servomotor |
|  | 6 |  | TPS | throttle position sensor |
| grey | 7 | blue/white | BLOCK through diode | neutral relay |
| black | 8 | blue/yellow | BLOCK | input 2 (use like blocking - side stand switch) |
| yellow | 9 | white/blue | CKPS (1) | input for pick-up 1 |
|  | 10 |  | IC 2 | inductive coil 2 |
| blue | 11 | black | GND | ground |
|  | 12 |  | POWEROUT 2 | poweroutput 3 (gear shift light) |
| red | 13 |  | + 12 V | supply 12 V (from ignition key) |
|  | 14 |  | POWEROUT 3 | poweroutput 3 (Power jet) |
|  | 15 |  | TACHO | output for tachometer |
| blue | 16 |  | SENSE GND | ground for sensors |
| white/red | 17 |  | + 5 V | supply for sensors |
| white/blue | 18 |  | STPS | servo position sensor |
| green | 19 | black/white | KILL SWITCH | input 1 |
|  | 20 |  | CKPS (2) | input for pick-up 2 |
| thin violet |  | black/yellow |  | trigger for servocontroller |

Outputs marked by green color you must connect direct to 5wire exhaust valve motor.

Red wire you must connect to +12V from ignition key.

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz