SPARKER DCCDIP2 - mounting instructions for Yamaha TZ250

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see table). Counterpart connectors are included.

| pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- |
| 1 | orange | IC 1 | inductive coil 1 |
| 2 | white/black | GND | ground (use for pickup gnd) |
| 3 | white | POWEROUT 1 | power output 1 - used for powerjet |
| 4 | black/red | M | output for servomotor |
| 5 | black/brown | M | output for servomotor |
| 6 |  | TPS | throttle position sensor |
| 7 |  |  |  |
| 8 | brown/white | INPUT 2 | multifunctional input 2 -use for quickshift |
| 9 | white/green | PICK-UP 1 | input for pick-up 1 |
| 10 | grey | IC 2 | inductive coil 2 |
| 11 | black | GND | power ground |
| 12 |  | POWEROUT 2 | power output 2 |
| 13 | red | + 12 V | supply 12 V |
| 14 | pink | POWEROUT 3 | power output 3 - used for powerjet |
| 15 |  | TACHO | output for tachometer |
| 16 |  | SENSE GND | ground for sensors |
| 17 | yellow/blue | + 5 V | supply for sensors |
| 18 | white/red | STPS | servo position sensor |
| 19 | black/white | INPUT 1 | multifunctional input 1 - used for kill switch |
| 20 | white/blue | PICK-UP 2 | input for pick-up 2 |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz