SPARKER DCCDIP2 - mounting instructions for Yamaha XT600

Wiring

Wiring must be done according the table below. You have to connect to DCCDIP2 unit power supply +12V (original unit has not this connection). It should key switched +12 V (brown goes from ignition key switch).

XT600 (1984-86), XT600Z TÉNÉRÉ (1983-85)

| SPARKER DCCDIP2 | motorbike wire color | original unit wire color | note |
| --- | --- | --- | --- |
| 2/blue | green | green | ground for CKPS |
| 20/brown | white/red | white/red | CKPS (high advance) |
| 9/yellow | white/ green | white/green | CKPS (low advance) |
| 13/red |  |  | key switched + 12 V |
| 11/blue | black | black | ground |
| 1/orange | orange | orange | induction coil |
| 19/grey/red | black/ white | black/ white | engine stop switch |

XT600 with side stand (from 1987)

| SPARKER DCCDIP2 | motorbike wire color | original unit wire color | note |
| --- | --- | --- | --- |
| 2/blue | black/yellow | green | ground for CKPS |
| 20/brown | blue/yellow | white/red | CKPS (high advance) |
| 9/yellow | green/white | white/green | CKPS (low advance) |
| 13/red |  |  | key switched + 12 V |
| 11/blue | black | black | ground |
| 1/orange | orange | orange | induction coil |
| 19/grey/red | black/ white | black/ white | engine stop switch |
| 8/black through diode | light blue + blue | light blue + blue | NEUTRAL switch + light |
| 8/black | blue/yellow | blue/yellow | side stand switch |

XT600Z TÉNÉRÉ with starter (1986-87)

| SPARKER DCCDIP2 | motorbike wire color | original unit wire color | note |
| --- | --- | --- | --- |
| 2/blue | green | green | ground for CKPS |
| 20/brown | red | white/red | CKPS (high advance) |
| 9/yellow | green/white | white/green | CKPS (low advance) |
| 13/red |  |  | key switched + 12 V |
| 11/blue | black | black | ground |
| 1/orange | orange | orange | induction coil |
| 19/grey/red | black/ white | black/ white | engine stop switch |
| 8/black | blue, blue/yellow | blue, blue/yellow | clutch, blocking input |

XT600Z (U) TÉNÉRÉ with starter (from 1988)

| SPARKER DCCDIP2 | motorbike wire color | original unit wire color | note |
| --- | --- | --- | --- |
| 2/blue | black/yellow | green | ground for CKPS |
| 20/brown | blue/yellow | white/red | CKPS (high advance) |
| 9/yellow | green/white | white/green | CKPS (low advance) |
| 13/red |  |  | key switched + 12 V |
| 11/blue | black | black | ground |
| 1/orange | orange | orange | induction coil |
| 19/grey/red | black/ white | black/ white | engine stop switch |
| 8/black | blue, blue/yellow | blue, blue/yellow | clutch, blocking input |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz