SPARKER DCCDIP2 - mounting instructions for Yamaha YZF-R6 2002

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DCCDIP2 has various colors. (see tables). Counterpart connectors are included.

| wire color DCCDIP2 | pin no. DCCDIP2 | wire color motorbike | name | description |
| --- | --- | --- | --- | --- |
| orange | 1 | orange | IC 1 | inductive coil 1 |
| blue | 2 | black | SENSE GND | ground for sensors |
| violet | 3 |  | FUEL PUMPE RELAY | output for fuel pump relay |
|  | 4 |  | M | output for servomotor |
|  | 5 |  | M | output for servomotor |
| grey | 6 | yellow | TPS | throttle position sensor |
|  | 7 |  | BLOCK_A | blocking input (neutral sw.) |
| black | 8 | blue/black or black (near by white) | BLOCK | blocking input (sidetand sw.) |
| yellow | 9 | white/red | CKPS (1) | input for pick-up (1) |
| white | 10 | grey | IC 2 | inductive coil 2 |
| blue | 11 | black/blue | GND | ground |
|  | 12 |  | GEAR SHIFT LIGHT | output for gear shift light |
| red | 13 | red/black | + 12 V | supply 12 V |
|  | 14 |  | POWER JET | Power jet output |
| green/yellow | 15 | yellow/black | TACHO | output for tachometer |
|  | 16 |  |  |  |
| white/red | 17 | blue | + 5 V | supply for sensors |
|  | 18 |  | STPS | servo position sensor |
|  | 19 |  | KILL SWITCH | input for kill switch |
|  | 20 |  | CKPS (2) | input for pick-up (2) |