SPARKER TCI - mounting instructions for Ducati 900SS with Magnetti Marelli Digiplex unit

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCI has various colors. (see table). Counterpart connectors are included.

| SPARKER TCI | pin on Digiplex | note |
| --- | --- | --- |
| yellow | 2 | sensor (+) |
| blue | 1 | sensor ground (-) |
| red | 6 | key switched + 12 V |
| blue | 10 | ground |
| white | 9 | induction coil horizontal |
| orange | 11 | induction coil vertical |

View to original unit:

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz