SPARKER TCI - mounting instructions for Kawasaki KZ500

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCI has various colors. (see table). Counterpart connectors are included.

Distance between rotor and pick-up sensors must be change to circa 0.4 mm. It must be correct to this distance!

| SPARKER TCI | motorbike | note |
| --- | --- | --- |
| blue | blue | sensor ground |
| blue | red | sensor ground |
| brown | yellow | CKPS 2, 3 |
| yellow | black | CKPS 1, 4 |
| red | red/yellow | key switched + 12 V |
| blue | black/yellow | ground |
| orange | black | induction coil 1, 4 |
| white | green | induction coil 2, 3 |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz