SPARKER TCI - mounting instructions for Loncin ATV300

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCI has various colors. (see table).

| wire color TCI | wire color original unit | motorbike | note |
| --- | --- | --- | --- |
| blue | green/white | green/white | sensor ground |
| yellow | blue/white | blue/white | CKPS |
| red | red | black | key switched + 12 V |
| blue | green | green | ground |
| orange | black/yellow | black/yellow | induction coil |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz