SPARKER TCI - mounting instructions for Suzuki LS650 SAVAGE

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER TCI has various colors. (see table). Counterpart connectors are included.

| SPARKER TCI | motorbike | note |
| --- | --- | --- |
| blue | green ? | sensor ground |
| yellow | orange ? | CKPS |
|  | black | signal START |
| red | orange/white | key switched + 12 V |
| blue | black/white | ground |
| orange | black/yellow | induction coil |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz