SPARKER DC-CDI-P - mounting instructions for Honda NSR125

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DC-CDI-P has various colors. (see table). Counterpart connectors are included.

| wire color DC-CDI-P | wire color motorbike | description |
| --- | --- | --- |
| orange | black/yellow | inductive coil |
| green/yellow | white/red | output for tachometer |
| yellow | blue/yellow | input for pick-up |
| blue | green | ground |
| green | black/white | kill switch |
| red |  | supply 12 V (black from ignition key) |
| black | green/white | blocking from side stand |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz