SPARKER DC-CDI-P - mounting instructions for Suzuki Freewind

Wiring

Wiring must be done according the table below. The wires of ignition SPARKER DC-CDI-P has various colors. (see table).

| wire color DC-CDI-P | wire color motorbike | name | description |
| --- | --- | --- | --- |
| orange | white/blue | IC | inductive coil |
| yellow | blue | CKPS | input for pick-up |
| blue | black/white | GND | ground |
| blue | green | GND | ground for CKPS |
| violet | green/blue | GEAR SHIFT LIGHT | output for gear shift light (use for solenoid) |
| red | orange/white | + 12 V | supply 12 V |
| green/yellow | black/red | TACHO | output for tachometer |

Producer address: 	IgniTech

Ceskobratrska 84

535 01 PRELOUC

Czech Republic

ignitech@ignitech.cz

www.ignitech.cz